Floating point numbers

In C a floating point number has a very definite format. To start with it might be better to refer to integer and non-integer numbers also known as real numbers.

Real numbers

An example of a real number in binary format is 111.111

The integer part 111 is decimal seven (4 + 2 + 1)

The non integer part 0.111 is 0.5 + 0.25 + 0.125 = 0.875

Therefore 111.111 equals 7.875

Real binary numbers can be shifted right and left in exactly the same way the integer numbers can.
Shifting one place to the left multiplies the number by 2.
Shifting one place to the right divides it by 2.

We can therefore multiply 111.111 by 8 to get 111111 = 63
and say that 111.111 = 111111 divided by 8 = 63/8 = 7.875

In a similar way we can say 111.111 = 0.111111 x 8
equals (0.5 + 0.25 + 0.125 + 0.0625 + 0.03125 + 0.015625) x 8 = 0.9843754 x 8 = 7.875

Note: In the number 7.875, 7 (binary 111) is referred to as its LHS.
.875 (binary .111) is referred to as its RHS.

Converting a fraction to decimal or binary

A slight digression is required before going any further

Consider the fraction A/B where B > A.
To convert this to decimal we use a loop containing two lines of integer arithmetic.

The first line calculates (10 x A) /B which gives an answer between 0 and 9
The second line calculates the remainder of this sum which is (10 x A)%B
The first line is then repeated, however this time A is replaced by the remainder just calculated.

For binary conversion we replace the 10 by 2 and the division always gives a result of 0 or 1

Decimal to binary conversion

Consider the number 7.875. We can process the LHS using familiar integer conversion. For the RHS we use the fraction to binary routine.

Consider 0.875: It is equal to the fraction 875/1000 where 1000 is known as the denominator
The first bit on the RHS of the binary point is 2 x 875/1000 = 1750/1000	1
This sum generates a remainder of 750
(750 x 2) /1000 is 1 remainder 500 and therefore the second bit is also 1
(500 x 2)/1000 is 1 remainder zero. Therefore the third and final bit is also 1

And we get 0.875 = 0.111 in binary.
Note: 875 are referred to as decimal places and 111 as binary places.

Setting the number of significant bits

The number 7.875 has 3 decimal digits following the decimal point.
It also has 3 bits following the binary point.
However the number of these bits will vary greatly and it may be necessary to limit them.

Consider the number 7.877. This is equal to 111.bbbbbbbbbbbbbbb.
The fraction to binary routine generates one bit for each division.
We therefore set the number of divisions to the number of significant bits for which there is space.

The floating point format allows 24 bits for the real number.
The number 7.875 requires 3 bits for the integer part.
When calling the fraction to binary routine we specify that 21 divisions are required and 0.875 is converted to binary 0.111000000000000000000000

Assembling a floating point number (FPN)

The bits in our sample number 111.111 with be shifted to 1.11111 and the exponent will be set to 2. The single 1 on the LHS of the binary point will not be saved since it is always present. Lagging zeros will be added to the RHS of the binary point until 23 bits are occupied as shown below:

11111000000000000000000

The steps required to achieve this are as follows:

Convert the integer part of the real number to binary and save it as a long integer
Determine the length (n) of this integer
Shift the integer by (24 - n) bits so that its MSB occupies bit 23
Convert the RHS of the real number to a long integer
Perform the decimal to binary conversion repeating the division process (24 – n) times
The LHS and RHS of the binary number can now be combined using the OR function

Note: As can be seem from the sample number the exponent is given by n – 1.

Bits 23 to 31 are used for the exponent. 127 is added to it before it is saved. An exponent of 2 is therefore saved as 129. Similarly other exponents are saved as follows:

-126	as	1
0	as	127
+127	as	254

This arrangement allows zero and 255 (all ones) to be reserved for underflow and overflow (to be discussed later).

Note: Bit 23 (the single 1) on the LHS of the binary point is over written by the exponent.

Binary to decimal conversion

Consider the binary number 0.111
We can shift this to the LHS of the binary point without changing its value provided we remember to divide the result by 8.
Therefore 0.111 = binary 111 divided by 8 which equals 7/8

This is converted to decimal using a fraction to decimal routine as shown below:

We start with 7/8
70/8 is 8 remainder 6
60/8 is 7 remainder 4
40/8 is 5 remainder zero
We therefore get 7/8 = 0.875

A first sketch: Non-integer number IO (input and output)

Reads a string containing decimal characters such as 7.875.
Converts them to a binary number as described above
Reconverts the binary form back to a decimal string and saves it.
Checks for any errors resulting from this process

Of course subroutines are also required to input data strings from the PC keyboard and output them to the screen. To avoid confusion these are not part of the sketch but are placed in a separate C file.

String from KBD
Separate out RHS side and convert to binary
Separate out LHS